## Slide 1: Pipelining: Basic and Intermediate Concepts Appendix C
Basics of Pipelining
Implementation of Pipeline
Hazards and their Solutions
Exception Handling
Pipeline with Floating-Point Instructions
Dynamic Scheduling of Pipelines

## Slide 2: Putting It All Together – MIPS R4000 Pipeline
EX: Execution cycle, includes:
Effective address calculation
ALU operation
Branch target computation
Condition evaluation
DF: First half of data fetch
First half of D-cache access
DS: Second half of data fetch
Completion of D-cache access
TC: Tag check
D-cache access hit or miss is determined
WB: Write back for loads and register-register operations
Substantial increase in amount of forwarding required

## Slide 3: Putting It All Together – MIPS R4000 Pipeline
Increase in both load and branch delays take place
Branch delay is of three cycles
Uses predict-not-taken strategy
There are four possible sources of forwarding
EX/DF, DF/DS, DS/TC and TC/WB
MIPS 4000 Floating Point Pipeline
Reading Assignment
Performance of R4000 Pipeline
Four major causes of stalls
Load stalls
Branch stalls
FP result stalls
FP structural stalls
There is extra penalty for deeper pipeline

## Slide 4: 2-cycles Load delay

## Slide 5: 3-cycles Branch delay

## Slide 6: Crosscutting Issues
RISC Instruction Sets and Efficiency of Pipelining
Simpler instruction sets make it easier to schedule code in a pipelined architecture
Recent pipelined implementations of complex instruction set
Translate complex instructions into simple RISC-like operations
Pentium III and Pentium IV
Dynamically Scheduled Pipelines
Static scheduling is done by compilers
Dynamic scheduling is performed by processors to solve the problem of too many stalls
Score-boarding technique of CDC 6600
To be discussed later

## Slide 7: Fallacies and Pitfalls
Pitfalls
Unexpected execution sequences may cause unexpected hazards
WAW hazards should never occur in a code sequence
When the sequence is unexpected, they may occur
Extensive pipelining can impact other aspects of a design leading to overall lower cost/performance
Two implementations of VAX
8600, 8650 and 8700

## Slide 8: Pipelining
Pitfalls ..
Evaluating a compile time scheduler on the basis of unoptimized code
Unoptimized code contains redundant loads, stores and other operations that might be eliminated by an optimizer
Concluding Remarks
Following were becoming common in microprocessors and also in high-end embedded processors by the early 1990s
Use of pipelining
Sophisticated dynamically scheduled pipelines
Multiple-issue approaches

## Slide 9: Instruction-Level Parallelism and Its Exploitation
Instruction-Level Parallelism
Types of Dependences
Compiler Techniques for Exposing ILP
Dynamic Branch Prediction
Dynamic Scheduling of Pipelines

## Slide 10: Instruction-Level Parallelism: Concepts and Challenges
Overlap among instructions is referred to as ILP
Techniques for extending and increasing the amount of parallelism exploited among instructions
Limitations are imposed by data and control hazards
Increase the ability of processor and compiler to exploit parallelism
Both hardware and software approaches are explored that exploit parallelism
Dynamic techniques depend on hardware to discover and exploit parallelism dynamically
These are the more dominating techniques
Static or compiler intensive approaches rely on software based methods to exploit parallelism
Have more limited use like in well-structured scientific applications with significant DLP

## Slide 11: Concepts and Challenges of ILP
Discuss features of both programs and processors that limit the amount of parallelism that can be exploited among instructions
Critical mapping between program structure and hardware structure
Pipeline CPI = Ideal Pipeline CPI + Structural Stalls + Data Hazard Stalls + Control Stalls
Ideal Pipeline CPI is a measure of the maximum performance attainable by the implementation
Reducing each of the terms on the right results in minimizing the overall pipeline CPI
Various techniques are used to reduce the components
Define the concepts on which these techniques are built
Determine the limits on how much parallelism can be exploited

## Slide 12: Major Techniques and the component of CPU equation that the Technique Affects

## Slide 13: Instruction-Level Parallelism
What is Instruction Level Parallelism?
Amount of parallelism available within a basic block is quite small
Basic block: A straight line code sequence with no branches in except to the entry and no branches out except at the exit
Exploit ILP across multiple basic blocks
Exploit parallelism among iterations of a loop
Loop-level parallelism
for (i = 0; i <= 999; i = i+1)
x[i] = x[i] + y[i];
Loop-level parallelism can be converted into ILP by unrolling loop either statically or dynamically
Another alternative is to use vector instructions
Used in both SIMDs and GPUs

## Slide 14: Instruction-Level Parallelism
Data Dependences and Hazards
Determining how one instruction depends on another is critical
To determine how much parallelism exists in a program
How that parallelism can be exploited
If two instructions are parallel, they can execute simultaneously in a pipeline without causing stalls
Dependence of one instruction on another is the key issue
There are three types of dependences
Data dependences
Name dependences
Control dependences

## Slide 15: Instruction-Level Parallelism
Data Dependences
Also called true data dependences
Instruction j is data dependent on instruction i if either of the following is true
Instruction i produces a result that is used by instruction j, or
Instruction j is data dependent on instruction k and instruction k is data dependent on instruction i
If two instructions are data dependent they cannot execute simultaneously or be completely overlapped
Dependences are a property of programs
Whether the dependence actually results in a hazard and whether that hazard actually causes a stall are properties of pipeline organization

## Slide 16: Dependences in RISC V code sequence

## Slide 17: Dependences in RISC V code sequence

## Slide 18: Dependences in RISC V code sequence

## Slide 19: Instruction-Level Parallelism
A data dependence conveys three things
Indicates the possibility of a hazard
Sets the order in which results must be calculated
Sets an upper bound on how much parallelism can possibly be exploited
Dependence limits the amount of ILP that can be exploited
Dependence can be overcome by
Maintaining the dependence but avoiding a hazard
Scheduling of code both in hardware and software
Eliminating a dependence by transforming the code
A data value can flow either through registers or through memory locations
Dependence through registers are easier to detect but dependence through memory locations is not

## Slide 20: Instruction-Level Parallelism
Name Dependences
Occurs when two instructions use the same register or memory location called a name but
There is no flow of data between the instructions associated with that name
There are two types of name dependences
Assuming i precedes j
Antidependence
When instruction j writes a register or memory location and instruction i reads it
Corresponds to a WAR hazard
Output dependence
When both i and j write to the same register or memory location
Ordering between instructions must be preserved
Preserved by detecting WAW hazard

## Slide 21: Instruction-Level Parallelism
Both antidependence and output dependence are only name dependences
Instructions can execute simultaneously or can be reordered if the name is changed
Register renaming: Can be done either statically by a compiler or dynamically by the hardware
Control Dependences
Determines the ordering of an instruction i with respect to a branch instruction so that
The instruction i is executed in correct program order and only when it should be
Every instruction except those in the first basic block is control dependent on some set of branches

## Slide 22: Instruction-Level Parallelism
There are two constraints
 An instruction that is control dependent on a branch cannot be moved before the branch so that, its execution is no longer controlled by the branch
 An instruction that is not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
Control dependence is preserved by the property in simple pipelines by
Executing instructions in program order
Detection of control or branch hazard ensures that an instruction that is control dependent on a branch is not executed until the branch direction is known
Control dependence is itself not the fundamental performance limit

## Slide 23: Instruction-Level Parallelism
Two major properties critical to program correctness
Exception behavior and data flow
Exception behavior
Preserving it means any change in the ordering of instruction execution must not change how exceptions are raised in the program
Data flow
Branches make the data flow dynamic
Speculation: A code scheduling method
Helps with the exception problem
Allows to lessen the impact of control dependence while still maintaining the data flow
Control dependence is preserved by implementing control hazard detection that causes control stalls

## Slide 24: Exception Behavior
ADD x2, x3, x4
BEQ x2, x0, L1
LD x1, 0(x2)
L1:
ADD x1, x2, x3
BEQ x4, x0, L
SUB x1, x5, x6
L: . . .
OR x7, x1, x8
Data Flow

## Slide 25: Basic Compiler Techniques for Exposing ILP
Examine the use of simple compiler technology to enhance a processor’s ability to exploit ILP
Crucial for processors that use static issue or static scheduling
Basic Pipeline Scheduling and Loop Unrolling
Parallelism among instructions must be exploited by finding sequences of unrelated instructions that can be overlapped in the pipeline
Compiler’s ability to perform scheduling depends on
The amount of ILP available
The latencies of the Functional Units in the pipeline
FP unit latencies
Functional units are fully pipelined or replicated
Examine how compiler increases the amount of available ILP by transforming loops

## Slide 26: Latencies of Floating Point Operations

## Slide 27: Loop Unrolling and Pipeline Scheduling
Example code for loop unrolling
for (i = 999; i >= 0; i = i - 1)
x[i] = x[i] + s;
Loop: fld f0, 0(x1)
fadd.d f4, f0, f2
fsd f4, 0(x1)
addi x1, x1, -8
bne x1, x2, Loop
Use latencies to calculate the total time to execute one iteration of the loop - 9 clock cycles
By scheduling, the time required is only 7 clock cycles
The ILP and the basic block size can be increased by using loop unrolling
Scheduling also improves with this technique